## Slide 1
ZTP Process
Obtain IP address through DHCP options
Option 66 (TFTP server)
Option 144 (Initial Configuration)
Obtain initial configuration from ZTP app
Contains all items to allow REST and SSH communication
Software
upgrade
required?
Upgrade switch (REST API)
VSF?
Provision Configuration (REST API)
VSF Master?
No
No
Yes
Yes
Provision Configuration (REST)
No
Yes
Completed
Completed
Provision VSF member (REST)
Renumber VSF member(SSH)
VSF member reboots
VSF member joins stack
VSF
standby
member?
Configure standby on master (SSH)
Completed
Completed
Provision VSF master (REST)
All VSF
members
joined?
No
No
Yes
Yes
Is VSF
standby back
online?
Admin
access verification
success?
No
Yes
No
Yes
Standby reboots
VSF master?
No
Yes
All VSF
members back
online?
Reboot switch (REST API)
Reboot master (REST API)
No
Admin
access verification
success?
No
Yes
1
1
21
100
100
100
100
21
22
22
23
3
6
9
9
4
4
4
4
41
41
5
6
41
42
41
42

## Slide 2
DHCP based process
Switch boots
Switch sends DHCP request
DHCP server sends response and DHCP ACK
ZTP app snoops DHCP ACK
Update ZTP device in app with IP address
Is device
configured for ZTP
(MAC address)?
Update DHCP tracker
Update DHCP tracker
DHCP server sends DHCP option 66 and 144
Switch knows where to download the initial config
No
Yes
ZTP app
Vendor class based:
Option 66 (TFTP server)
Option 144 (Initial Configuration)
For AOS-CX 6x00: ztpdhcp6k.cfg
For AOS-CX 8xxx: ztpdhcp8k.cfg
Initial configuration downloaded
App knows where to find the switch and has initial admin access

## Slide 3
Static IP address based process
Switch boots
Switch sends DHCP request
DHCP server sends response and DHCP ACK
ZTP device is configured for static IP address assignment
Infoblox
Static IP address
PHPIPAM
DHCP server sends DHCP option 66 and 144
Switch knows where to download the initial config
ZTP app
Vendor class based:
Option 66 (TFTP server)
Option 144 (Initial Configuration)
[mac address of the switch].cfg
Initial configuration downloaded
App knows where to find the switch and has initial admin access